## Slide 1: WATERWISE WORKSHOP
Presented by Kirstie MacDiarmid
Sustainability Advisor

## Slide 2: OVERVIEW
How to read your water bill
How to check for leaks
Different types of hot water systems
How to measure flow rates
How to save water in your home

## Slide 3: HOW TO READ YOUR BILL
Average Aucklander uses 140-175L per day
Waterwise goal 120L per day
Notes: This graph shows the average litres of water used for a particular household size and can be found on the back of your water bill.
To calculate yours: divide your daily usage by number of people in your home ‘daily usage’ is visible on the graph in the next slide.

## Slide 4: CHANGES IN WATER USE
Seasonal
Occupancy
Water heating system
Leaks
Household cleaning
Notes: What can change your water use:
Seasonal: Gardening in summer/longer showers in winter
Changes in occupancy (holiday away, family visiting)
Change in water heating system
Leaks
Household cleaning - e.g water blasting
Meter read every second month After a change in water use - it can take 4 months for (A) actual and (E) Estimate readings to ‘level out’.

## Slide 5: ONLINE WATERCARE ACCOUNT
Pay bills
Check account balance
View previous bills
Switch to e-billing
Notes: Register for My Account on the watercare website
Who can register?
If you want to set up your account online, you need to be an existing customer and have an account with us.
If you are a tenant, you can register using the water account details for your property. If you are an authorised tenant, you can take all of the actions below. If you are unauthorised, you can still register and pay your bills online.
Using MyAccount you can:
pay bills or set up direct debit
check your account balance
switch to or cancel e-billing
update contact details
view or print previous bills
apply for a leak allowance
print a copy of a past bill
connect to Xero.
You can also manage multiple accounts.
Before you register, please have your latest water bill handy.
We need to know:
your Watercare account number
the date on the bill
the balance on the bill.

## Slide 6: FINDING YOUR WATER METER
Usually at the front of the property
In a box with a blue or black lid
Lift the lid and look for the meter dial
Notes: Finding your meter
Most homes have their own water meter. This is usually at the front of the property, near the left or right boundary. In flats or apartments there may be only one meter for all the dwellings in each building.
Water meters are in the ground, in a box made of timber, plastic, concrete, or metal. The lid is usually blue or black. Lift the lid and you should see the meter dial. To read the dial, you may need to remove leaves and debris, or flip up the cover.
Some boxes may contain multiple water meters. These can be under one large metal lid. Ideally, identify your meter and label it. This means you can quickly locate and turn off your water supply if you have a sudden leak.
Your meter serial number
The number of your meter is on your water bill. See page 2, under ‘Consumption details’.
You can also find the number online using MyAccount

## Slide 7: LEAK TESTING
Choose 4 - 8 hours where you won't be using water
Write down the 8-digit number before and after
If there is a difference, you could have a leak
Notes: If you have looked in the previous location but haven’t found any signs of a leak it can be good to do a leak test
If the leak test shows you might have a leak and you can’t find where it is contact a plumber with leak detection equipment to find the leak and have it repaired.
Complete a leak test as soon as possible to identify whether or not a leak is contributing to your bill, then repair any detected leaks as soon as possible. Continue to perform a leak test twice yearly (daylight savings is a great time to do this, alongside smoke detector tests) or any time you have an unexpectedly high bill.

## Slide 8: LOOKING FOR LEAKS
Dripping taps/shower
Water dripping down back of toilet bowl
Behind appliances
Under the house
Damp patches garden/driveway
Notes: Where to look for leaks in and around your house:
Look for damp patches and cracked concrete in the garden, lawn or driveway during dry weather,
Look under the house, shine a torch on pipes and on the ground to check for drips or wet spots
Check if your hot water cylinder has wet patches around it or if water is dripping from the overflow pipe
Check if your toilet has a constant slow drip or trickle running down the back of the toilet bowl. Although it seems small, this can be enough water loss to show up in a quick leak test, especially if multiple toilets are leaking.
Listen for running water within your property when no taps, hoses or showers are turned on
Look for drips or wet areas at your taps and behind appliances like dishwasher and washing machine
Look for mould or dampness on floors and walls

## Slide 9: TOILET LEAK TESTING
Take a square of toilet paper
Place it on the back of the bowl
If the toilet paper gets wet, you have a leak
Notes: A toilet leak is very common and usually due to the flapper in the cistern not be able to seal and can usually be fixed by replacing a washer.
In the meantime you can turn off the water supply overnight or when not in use via the tap.

## Slide 10: LEAK ALLOWANCE
Apply for after leak is fixed
Partial credit to next bill
Maximum of four consecutive bills
Notes: Once leak is repaired you can apply for a leak allowance by filling out a form found on the watercare website or you can apply through your watercare account.
The amount refunded will depend on the difference in water use during the time you had the leak against the same time the last year. If you have not been at the property for a whole year the average will be taken.
Watercare can reimburse wastewater charges over the period that there has been a leak. Once all leaks are fixed, complete a leak allowance application. If it is unclear when the leak began, Watercare may need to wait a few months before reimbursing you while they figure out what your standard water use is. Make sure you keep your plumbers invoice, to use as a supporting document for your application. Visit the Watercare website and download a leak allowance application form or apply online by setting up and logging into ‘My Account’.
You can only apply once every two years, so only apply for a reimbursement for large leaks.

## Slide 11: HOT WATER SYSTEMS
Notes: Mains Pressure Systems:
Mains pressure Electric Cylinder
Gas hot water cylinder
Gas califont
Heat pump hot water Cylinder
Low Pressure Systems:
Low pressure hot water cylinder
Some solar powered hot water cylinders
How to save on your power bill - could save you up to $60/year
Lag pipes - $6/meter
Wrap your hot water cylinder (if you can cover ¾ +) - $70
Next time you have a plumber/ electrician on site, get them to check that your cylinder is set at 60 degrees.

## Slide 12: HOT WATER SYSTEMS
Low Pressure | MAINS Pressure
The shower temperature changes when someone uses hot water elsewhere | No change in shower temperature when water used elsewhere
Hot tap has less pressure than cold tap | Hot and cold taps have same pressure
You can stop the flow of hot water with you thumb | You cannot stop the flow of hot water with your thumb
A metal overflow pipe sticks out of your roof | Instantaneous hot water with no storage or gas heated system
Notes: If you have an electric water cylinder, you will need to find out whether it is Low pressure (30 - 120 kPa) or Mains pressure (120 - 1100 kPa). If this isn't written on your cylinder. Some electric hot water cylinders may also be outside, in a casing.
You cannot install flow restrictors on a low pressure system

## Slide 13: WHERE TO SAVE WATER
Shower and laundry combined uses 50% of your overall water use

## Slide 14: FLOW RATES
Check how much water your taps/shower uses
6L/min ideal for taps
9L/min ideal for showers
Notes: Hot water temperature: Ideally around 55 degrees at the tap.
(don’t have a thermometer at home? Borrow a heat kit from your library)

## Slide 15: SAVING WATER - BATHROOM
Install water saving devices
4 minute showers, one per person per day
Reduce capacity toilet cistern
Notes: Try to get everyone in the household to spend no more than 7 minutes in the shower. Water use in the shower and laundry combined, represents around half of your household water use. Therefore, good savings can be made through small changes. The waterwise goal is a 4 minute shower. You can also use less water by turning the shower off while shaving, soaping up, and washing hair. If you have a hot water cylinder, short showers will help you save on your electricity bill too.
Reduce the capacity of your cistern and the amount of water used per flush.
First - turn the tap off at the wall and flush, to empty the cistern and prevent any spills! Fill jars or a 1 or 2 L bottle with water and screw the lid on. Place it/them inside the toilet cistern, ensuring they won’t float about and knock the plumbing. Then turn the tap back on to refill the cistern.

## Slide 16: SAVING WATER - KITCHEN
Install tap aerators or half lift the tap
Run dishwasher when full and use ECO setting
Compost instead of using waste disposal
Notes: Use a plug or bowl in the sink when washing food or dishes. Consider recycling the wash/rinse water over non-edible gardens or use it to run the waste disposal unit.
Consider using the Eco setting/ Water Save setting when doing laundry and/or using your dishwasher, this may make the wash cycle longer but will save on energy and water consumption in most modern machines.
Consider using your kitchen wash/rinse water on non edible plants OR to run the waste disposal unit. You can also reduce waste disposal use by collecting scraps in a container and emptying them once per day.
Consider composting your food scraps. There are several ways to compost, including bokashi which you can keep in a kitchen cupboard (it doesn’t smell!). Learn more about these composting systems with a free workshop from Compost Collective and earn a $40 discount on purchasing a compost system, find a free workshop in your area via www.compostcollective.org.nz.

## Slide 17: WATER SAVING DEVICES
Tap Aerator
Flow Restrictor
Shower Timer
Low flow shower head
Notes: Flow Restrictor
This is installed inside the shower hose
This reduces your shower flow rate down to approx. 9 litres per minute.
Option to buy low flow shower head instead.
Tap Aerator
This is fitted onto the end of bathroom or kitchen taps
This reduces your tap flow rate down to 9 or 6 litres per minute.
Remember. Don’t install tap aerators and flow restrictors on low pressure hot water systems unless there is a non return Valve on your low pressure cylinder. Otherwise restricted water can flow back into your cylinder and could result in needing to replace it. (generally low pressure systems don’t need restriction anyway.)
Low flow Shower Head
Some low flow shower heads can still feel great below 9L per minute. But ideally test them first at a show room to make sure you are happy with the feel. Reducing flow rates to an unsatisfying feel can cause people to shower longer.
Reduce the shower flow rate with a low flow shower head. 9 litres per minute, or 3 blue stars is an efficient flow rate. In most Chesters Plumbing & Bathroom showrooms you can test low flow showerheads. Methven sometimes provide free shower head trials that can be worth considering.
Shower Timer
This is stuck inside the shower wall
This runs for approximately 5 minutes. When all the sand is gone – it’s time to jump out of the shower!
Gizmo
This goes in the toilet cistern (for older toilets with a large cistern).
This gives you precise control over the amount of water that flushes through the toilet.

## Slide 18: INSTALLING THESE DEVICES

## Slide 19: COLLECTING GREY WATER
Use bowl or plug when washing dishes
Use bucket while shower is warming up
Reuse this water for non edible gardens or your waste disposal
Notes: Use a plug or bowl in the sink when washing food or dishes. Consider recycling the wash/rinse water over non-edible gardens or use it to run the waste disposal unit.

## Slide 20: SAVING WATER - LAUNDRY
Only wash full loads
Use ECO setting
If buying a new machine, consider a front loader
Use cold washes
Notes: Where possible, try limiting the amount of washing being done. Water use in the laundry and shower combined, represents around half of your household water use! Therefore, good savings can be made here through small changes! Reusing towels can reduce washing, just hang them outside or on a heated towel rail in your bathroom to dry between uses. If drying inside, remember to open a window and close the door so moisture doesn’t make its way into the rest of the house.
Consider using the Eco setting/ Water Save setting when doing laundry and/or using your dishwasher, this may make the wash cycle longer but will save on energy and water consumption in most modern machines.
Wash full loads of laundry whenever possible as half loads still use about 70% of the water a full a load uses.

## Slide 21: SAVING WATER - OUTDOORS
Use a trigger on your hose
Use mulch
Water in the morning or late afternoon
Water plants every 2-3 days
Rainwater harvesting
Notes: Consider harvesting rain for your outdoor water requirements. A basic rain harvesting system for outdoor use doesn’t have to cost more than $150 and can usually be installed by yourself without consents. More robust systems can be purchased from hardware stores and tank suppliers. You can also add a small pump if needed to give you more pressure.
Consider putting mulch around garden beds, shrubs and fruit trees to retain up to 70% of moisture, suppress weed growth, and add nutrients to the soil. Remember not to put the mulch against the tree trunk - leave a ring between the trunk and the mulch. For mulch, you can use wood chips, dried leaves or grass clippings (Tip: Seed-free is best. Spread out grass clippings on concrete for two days before using them. This dries them out and stops them clumping together).
Watering less frequently promotes deeper and stronger root growth, every 3 – 5 days that pass without rain is usually enough. Watering in the morning or late afternoon allows the water be absorbed before it evaporates.
Take a look at our ‘build your own rain harvesting kit’ in our online resources or grab a flyer.

## Slide 22: THANK YOU NGA MIHI
Find us at:
www.ecomatters.org.nz/homes
water@ecomatters.org.nz